## Slide 1: Arduino Bluetooth Workshop
By IEEE

## Slide 2: Agenda
Introduction to Bluetooth
Using Bluetooth with an Arduino
Practice Time

## Slide 3: What is Bluetooth?
Famous Short Range Communication / Data Transfer Technology
Commonly found in mobile phones, computers and other electronic devices
Many versions:
  1.0, 1.1, 1.2 … 3.0, 4.0 (LE), 4.1, 4.2, 5.0

## Slide 4: Bluetooth Concepts
Great Intro:
  https://learn.sparkfun.com/tutorials/bluetooth-basics/all
Each Bluetooth Device has a unique MAC Address
Connection Process: Refer to link above!
Bluetooth Profiles:
  Serial Port Profile (SPP)
  Human Interface Device (HID)

## Slide 5: Applications in robotics / Engineering
Wireless Control in short-range (E.g. Android Bluetooth Controller App)
Automated Wireless Data Communication between Devices (E.g. Swarm Unit)
Mesh Network (E.g. Beacons for position tracking)
Wireless collection of data from sensors

## Slide 6: Bluetooth With Arduino
BUILT IN VARIANTS | ARDUINO COMPATTIBLE MODULES
BLEduino | HC-05
ATmega328-BT | HC-06
Arduino Bluno | 
Arduino Primo | 

## Slide 7: The HC-05 Bluetooth Module
Bluetooth 2.0 + EDR (Enhanced Data Rate)
Implements a SPP (Serial Port Profile)
Can be both master and slave

## Slide 8: The HC-05 Bluetooth Module
VCC : Standard Power (3.3v)
GND : Ground
RX : Receive
TX : Transmit
EN : Key
STATE: LED

## Slide 9: The HC-05 Bluetooth Module
How to configure?
  Connect as shown
    RX to RX; TX to TX !
  Enter AT-Mode by setting EN Pin to HIGH (5V)
  Use Serial Monitor on Arduino IDE (SHIFT + CTRL + ‘M’)
    Baud Rate: 38400; Use ‘Both NL and CR’
  LED on HC-05 should blink 1 / 2s

## Slide 10: AT-Mode for HC-05 (Basic Commands)
Command | Response | Parameter
AT | OK | NONE
AT+NAME=<PARAM> | OK | Param: Bluetooth device name Default: “HC-05”
AT+NAME? | +NAME: <PARAM> OK----success 2. FAIL----failure | 
AT+PSWD=<PARAM> | OK | Param: Pin Code Default: “1234”
AT+ PSWD | + PSWD ：<Param> OK | 

## Slide 11: How to Use After Configuring?
The Bluetooth module will simply act as a serial connection to the device its connected to.
Swap RX and TX wires
Remove wire from GND to Reset
Baud Rate: 9600
Use Serial.read() / Serial.write()
Refer to ‘Bluetooth_Switch.ino’
Remove this
Swap these

## Slide 12: Schematic to control an LED
Connect as shown

## Slide 13: How to Connect to the HC-05
Through phone
  Download ‘Arduino Bluetooth Control’
  https://play.google.com/store/apps/details?id=com.app.control&hl=en
Through PC
  http://www.collideabq.com/2016/04/28/bluetooth-serial-connection-with-windows-10/
  Use pyserial to communicate to Arduino via Python
  Please refer to this in your free time

## Slide 14: HC-05 through Phone
Connect to HC-05
Use Buttons Mode
Send data!

## Slide 15: Try it yourself (30 min)
Play around with the different modes of sending data to the HC-05
Try and make a simple game to play between your phone and Arduino
  Eg. A memory game?

## Slide 16: Useful Links
Master and Slave: http://www.instructables.com/id/How-to-Configure-HC-05-Bluetooth-Module-As-Master-/
Bluetooth Controlled Projects: http://www.instructables.com/id/Bluetooth-Controlled-Projects/

## Slide 17: THANK YOU  SUTD IEEE STUDENT BRANCH