## Slide 1: Digital Electronics Crash course – day 1
21-AUG-2018
Abhimanyu Arora
Koh Yi Min Jason

## Slide 2: Table of content
Day 1 1) Binary/Hexadecimal/BCD
2) Signed/Unsigned number
3) Binary and Hexadecimal addition
4) Logic gates circuits and Boolean Algebra
5) Implementing/simplifying logics gates
6) SOP (Sum-Over-Product), POS (Product-Over-Sum) and K-map
Day 2
7) Clock Signal and flip-flops (SR, JK, T, D)
8) D flip-flop state machine
9) Multiplexer, Comparator and De-Multiplexer
10) Encoder, Decoder, decade counter, up/down synchronous counter and ripper counters
11) 7-Segment display, 7-Segment display decade counter and BCD to 7-segment display driver

## Slide 3: Binary/Hexadecimal/BCD

## Slide 4: Binary
What is Binary?
In order for computers to perform any logical/arithmetic operation on numbers, it has to be converted to Binary.
Binary is a number system that has a radix (base) of 2.
A binary digit is called a bit and 8 bits is called a byte.
In a binary number, the binary digit at the right end is called the Least Significant bit (LSB) and the binary digit at the left end is called the Most Significant bit (MSB)

## Slide 5: Binary
Decimal number system - In the decimal number system, each Digit (D) has a position value (PV) of 10n where n is the position number - Each Digit (D) has 10 symbols (0, 1, 2, 3, 4, 5, 6, 7, 8, 9) - The Digit at the right end has a position number of 0. It is called the “ones place” - The Value of Digit (VD) is equal to Position Value (PV) multiply by the Digit (D) VD = PV x D
Example: 4057 = VD3 + VD2 + VD1 + VD0 4057 = (D x PV)3 + (D x PV)2 + (D x PV)1 + (D x PV)0 4057 = (4 x 103) + (0 x 102) + (5 x 101) + (7 x 100) 4057 = 4057

## Slide 6: Binary
Binary number system In a Binary number system, each Digit (D) has a position value (PV) of 2n where n is the position number The Digit at the right end has a position number of 0. It is called the “one places”
In a binary number system, each Digit (D) has 2 symbols (0 and 1) The Value of Digit (VD) is equal to Position (PV) Value multiply by the Digit (D) VD = PV x D
Example: 1011 0101 = VD7 + VD6 + VD5 + VD4 + VD3 + VD2 + VD1 + VD0 1011 0101 = (D x PV)7 + (D x PV)6 + (D x PV)5 + (D x PV)4 + (D x PV)3 + (D x PV)2 + (D x PV)1 + (D x PV)0 1011 0101 = (1 x 27) + (0 x 26) + (1 x 25) + (1 x 24) + (0 x 103) + (1 x 102) + (5 x 01) + (7 x 10) 1011 01012 = 1011 01012 = 18110

## Slide 7: Decimal to Binary
Aesef
Decimal to Binary (Method #1 - Divided by 2) To convert from Decimal to Binary, we take the decimal number and keep performing a whole number division by 2 till we get 0
The remainders of the quotient will be the binary number. The largest position value is at the bottom
Operation | Quotient | remainders
114 ÷ 2 | 57 | 0
57 ÷ 2 | 28 | 1
28 ÷ 2 | 14 | 0
14 ÷ 2 | 7 | 0
7 ÷ 2 | 3 | 1
3 ÷ 2 | 1 | 1
1 ÷ 2 | 0 | 1
Example:1 Convert 11410 to Binary
Answer: 111 00102
1 1 1 0 0 1 0

## Slide 8: Decimal to Binary
Example:2 Convert 26110 to Binary
Example:3 Convert 19910 to Binary

## Slide 9: Decimal to Binary
Decimal to Binary (Method #2 - Tables) Step 1: We draw a table listing the all position values that is smaller than the number Step 2: fills up “1” to the column correspond to the position values till the sums of all position values are equal to the number
Example:1 Convert 11410 to Binary
Answer: 111 00102
1 1 1 0 0 1 0
64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 1 | 0 | 0 | 1 | 0

## Slide 10: Decimal to Binary
Example:2 Convert 26110 to Binary using the table method
Example:3 Convert 19910 to Binary using the table method

## Slide 11: Binary to Decimal
Binary to Decimal Multiply each digit of the binary with its respective position value and sum all of them
Example:1 Convert 1110 00112 to decimal
Answer: 22710
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
= (128 x 1) + (64 x 1) + (32 x 1) + (16 x 0) + (8 x 0) + (4 x 0) + (2 x 1) + (1 x 1) = (128 x 1) + (64 x 1) + (32 x 1) + (2 x 1) + (1 x 1)
= 227

## Slide 12: Binary to Decimal
Example:2 Convert 0001 00012 to decimal
Example:3 Convert 1111 10012 to decimal

## Slide 13: Decimal to Hexadecimal
Aesef
Decimal to Hexadecimal Similar to convert from Decimal to Binary, we take the decimal number and keep performing a whole number division by 16 till we get 0
The remainders of the quotient will be the binary number. The largest position value is at the bottom
Operation | Quotient | Remainders (Decimal | Remainders (HexDecimal)
124 ÷ 16 | 7 | 12 | C
7 ÷ 16 | 0 | 7 | 7
Example:1 Convert 12410 to Hexadecimal
Answer: 7C16
7 C

## Slide 14: Decimal to Hexadecimal
Example 2: Convert 49310 to Hexadecimal

## Slide 15: Decimal to Hexadecimal
Example 3: Convert 219310 to Hexadecimal

## Slide 16: Hexadecimal to decimal
Hexadecimal to decimal Just like converting binary to decimal, we will multiply each digit of the hexadecimal with its respective position value and sum all of them
Example:1 Convert A316 to decimal
Answer: 16310
161 = 16 | 160 = 1
A | 3
= (10 x 16) + (3 x 1)
= 163

## Slide 17: Hexadecimal to decimal
Example:2 Convert E9B16 to decimal
Example:3 Convert D87F16 to decimal
Decimal | Hexadecimal
0 | 0
1 | 1
2 | 2
3 | 3
4 | 4
5 | 5
6 | 6
7 | 7
8 | 8
9 | 9
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F

## Slide 18: BCD number system
What is BCD
BCD (Binary-coded decimal) is a 4 bit binary number that has a maximum value of 10012 or 9 in decimal

## Slide 19: BCD number system
Decimal to BCD conversion To convert from decimal to BCD, we take individual digit in a decimal number and convert it to its respective 4 bit binary number
Example:1 Convert 9310 to BCD
9 3
1001
0011
Answer: 1001 0011BCD

## Slide 20: BCD number system
Example:2 Convert 42110 to BCD
Example:3 Convert 928110 to BCD

## Slide 21: Binary and Hexadecimal addition

## Slide 22: Binary and Hexadecimal addition
Binary and Hexadecimal addition
Just like adding in decimal, we can also add in binary and Hexadecimal

## Slide 23: Binary and Hexadecimal addition
Example:1 add 10011112 and 11101002 together
Example:1 add E9316 and FF16 together
1001111
1110100
+
11000011
1
1
1
E93
FF
+
F92
1
1
1
1

## Slide 24: Binary and Hexadecimal addition
Example:2 Add 11101012 and 111112 together
Example:3 Add 101110112 and 1111112 together
Example:2 Add AD916 and E7816 together
Example:3 Add FF2316 and DF5716 together

## Slide 25: Signed/Unsigned number

## Slide 26: Signed/Unsigned number
What are signed numbers? To represent negative numbers in binary, we need to use signed binary number system
An unsigned binary number system can only represent positive binary numbers We will learn 2’s compliment signed numbering representation, in this number system the Most significant bit has a negative position value of what that digit has in an unsigned number system

## Slide 27: Signed/Unsigned number
Converting decimal to signed binary number is different from converting decimal to unsigned binary number
Example:1 Convert -3410 to 2’s compliment signed binary number
Step 1:
Convert the -3410 to unsigned binary number as if you are converting 3410 to binary
1 0 0 0 1 02
Step 2:
Invert all the bits
1 0 0 0 1 02
0 1 1 1 0 12
Step 3:
Add 12 to the inverted value
0 1 1 1 0 12
12
+
0 1 1 1 1 02
Step 4:
Add the signed bit to the binary number
1 0 1 1 1 1 02
Value from step 3
Signed bit
= 1 0 1 1 1 1 02

## Slide 28: Signed/Unsigned number
Example:2 Convert -9910 to 2’s compliment signed binary number
Example:3 Convert -21210 to 2’s compliment signed binary number

## Slide 29: Logic gates

## Slide 30: Logics gates
What are logics gates? - Logic gates are electronic devices that implement a Boolean function. Condition in the logic gate’s inputs need to be met in order for the logic gate to output a TRUE.
There are 7 logics gate 1) NOT
2) AND
OR
NAND
NOR
XOR
XNOR

## Slide 31: Logics gates
NOT gate
NOT gates has only one input and one output
The NOT gate take the input signal and inverts it
Input | Output
A | Q
0 | 1
1 | 0
NOT gate symbol
NOT gate Truth Table
NOT gate Boolean expression

## Slide 32: Logics gates
AND gate
AND gates has minimum two inputs and one output. There is no limit to how many inputs an AND gate can have.
All inputs need to be TRUE in order to output a TRUE
Input |  | Output
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
AND gate Truth Table
AND gate Boolean expression
NOT gate symbol

## Slide 33: Logics gates
OR gate
OR gates has minimum two inputs and one output. There is no limit to how many inputs an OR gate can have.
Either one of the inputs need to be TRUE in order to output a TRUE
Input |  | Output
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
OR gate Truth Table
OR gate Boolean expression
OR gate symbol

## Slide 34: Logics gates
NAND gate
NAND gates has minimum two inputs and one output. There is no limit to how many inputs a NAND gate can have. ALL of the inputs need to be TRUE in order to output a FALSE NAND gates are AND gates with a NOT gate connected to its output
Input |  | Output
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NAND gate Truth Table
NAND gate Boolean expression
NAND gate symbol

## Slide 35: Logics gates
NOR gate
NOR gates has minimum two inputs and one output. There is no limit to how many inputs a NOR gate can have. Either one of the inputs need to be TRUE in order to output a FALSE NOR gates are OR gates with a NOT gate connected to its output
Input |  | Output
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR gate Truth Table
NOR gate Boolean expression
NOR gate symbol

## Slide 36: Logics gates
XOR gate
XOR gates has only two inputs and one output. Both inputs need to be on a different logic level in order to output a TRUE
Input |  | Output
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XOR gate Truth Table
XOR gate Boolean expression
XOR gate symbol

## Slide 37: Logics gates
XNOR gate
XOR gates has only two inputs and one output. Both inputs need to be same logic level in order to output a TRUE
Input |  | Output
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
XNOR gate Truth Table
XNOR gate Boolean expression
XNOR gate symbol

## Slide 38: Logics gates

## Slide 39: Implementing/simplifying logics gates

## Slide 40: Implementing Logics gate
Logics gate cascaded together to create desire logics outcome For example the picture shows an OR gate inputs are connected to the output of the NOT gate and AND gate. The Boolean expression for the circuit is Z = A’ + BC

## Slide 41: Implementing Logics gate
When given a Boolean expression. we need to know how to draw the logic circuits
Example:1 Implement the following logic Y = AB + C
Answer

## Slide 42: Implementing Logics gate
Example:2 Implement the following logic
Example:3 Implement the following logic

## Slide 43: Simplifying Logics gate
A Logic gate designer need to learn how to simplify any Boolean expression so that he could save components and money The Boolean expression below
can be simplified to

## Slide 44: Simplifying logic gate
Boolean Algebra rules
De Morgan's theorem
XOR equivalent

## Slide 45: Simplifying Logics gate
Example:1 Simplify the following logic
AA
A
A
0
0
1

## Slide 46: Simplifying logic gate
Example:2 Simplify the following logic
Example:3 Simplify the following logic

## Slide 47: Sum-Over-Product (SOP) , Product-Over-Sum (POS) and K-Map

## Slide 48: Sum-Over-Product (SOP) and Product-Over-Sum (POS)
Sum-Over-Product (SOP), Product-Over-Sum (POS) and K-map are 3 methods we can use to implement a Boolean expression from a truth table Both SOP and POS’s Boolean expression are not in its simplest form. SOP, POS and K-map can be use to implement a Boolean expression for any number of inputs correspond to one output

## Slide 49: Sum-Over-Product (SOP) and Product-Over-Sum (POS)
Example:1 Write the Boolean Expression of the following truth table using Sum-Over-Product (SOP) and Product-Over-Sum (POS)
Inputs |  |  | Output
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Answers:
(SOP answer)
(POS answer)
*NOTE Although we get a Boolean expression using SOP and POS but it is not in is simplest form. We still can simply it further.

## Slide 50: Sum-Over-Product (SOP) and Product-Over-Sum (POS)
For SOP, we look at the inputs state that correspond to a logic HIGH output and AND them together. For those inputs that are logic LOW, we will invert them before we AND them
To get the Boolean expression, we OR those AND expression together as shown
Inputs |  |  | Output
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
SUM-OVER-PRODUCT (SOP)

## Slide 51: Sum-Over-Product (SOP) and Product-Over-Sum (POS)
Inputs |  |  | Output
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
For POS, we look at the inputs state that correspond to a logic LOW output and OR them together. For those inputs that are logic HIGH, we will invert them before we AND them
To get the Boolean expression, we AND those OR expression together as shown
PRODUCT-OVER-SUM (POS)

## Slide 52: K-Maps (Karnaugh map)
K-Maps (Karnaugh map) can be use to implement a Boolean expression in its simplest form.
Below shows a K-map for 2 inputs, 3 inputs and 4 inputs
2 inputs K-map
3 inputs K-map
4 inputs K-map

## Slide 53: K-Maps (Karnaugh map)
Example:2 Write the Boolean Expression for the following truth table using a K-map
Inputs |  | Output
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Answer:

## Slide 54: K-Maps (Karnaugh map)
Step 1
Inputs |  | Output
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Copy the logic values of the output to the corresponding inputs on the K-map

## Slide 55: K-Maps (Karnaugh map)
Step 2
Group the ones together in groups of 2, 4, 8 or 16 as shown

## Slide 56: K-Maps (Karnaugh map)
Step 3
For each group, AND the input(s) that is common to the group. If the input is logic LOW, Invert it before AND them
A in logic LOW is common to the group
Hence the Boolean expression is

## Slide 57: K-Maps (Karnaugh map)
Step 4
OR all the groups Boolean expression
Since there is only one group which Boolean expression is , The
Boolean expression for the Truth Table is

## Slide 58: K-Maps (Karnaugh map)
Example:3 Write the Boolean Expression for the following truth table using a K-map
Inputs |  |  | Output
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Answer:

## Slide 59: K-Maps (Karnaugh map)
Inputs |  |  | Output
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Step 1
Copy the logic values of the output to the corresponding inputs on the K-map

## Slide 60: K-Maps (Karnaugh map)
Step 2
Group the ones together in groups of 2, 4, 8 or 16 as shown. Groups can overlap with each other

## Slide 61: K-Maps (Karnaugh map)
Step 3
For each group, AND the input(s) that is common to the group. If the input is logic LOW, Invert it before AND them

## Slide 62: K-Maps (Karnaugh map)
Step 4
OR all the groups Boolean expression

## Slide 63
Inputs |  |  |  | Output
A | B | C | D | Y
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Example:4 Write the Boolean Expression of the following truth table using a K-map
Answer:

## Slide 64
Inputs |  |  |  | Output
A | B | C | D | Y
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Step 1
Copy the logic values of the output to the corresponding inputs on the K-map

## Slide 65: K-Maps (Karnaugh map)
Step 2
Group the ones together in groups of 2, 4, 8 or 16 as shown. Groups can overlap with each other

## Slide 66: K-Maps (Karnaugh map)
Step 3
For each group, AND the input(s) that is common to the group. If the input is logic LOW, Invert it before AND them

## Slide 67: K-Maps (Karnaugh map)
Step 4
OR all the groups Boolean expression

## Slide 68: The END