## Slide 1: Line Following with PID
SUTD IEEE

## Slide 2: Objective: Follow A Line
ROBOT
But how do you follow a line?
  Keep the line in the center!

## Slide 3: Objective: Follow A Line
Open Loop System
  Use logic to control. If this is the input → what is the output?
Closed Loop System (With feedback)
  Input → Decision → Output → Input → …

## Slide 4: Open Loop System
INPUT (LEFT SENSOR ¦ RIGHT SENSOR) | OUTPUT
0 ¦ 0 | Move Forward
1 ¦ 0 | Turn CCW (Counter Clockwise)
0 ¦ 1 | Turn CW (Clockwise)
ROBOT
ROBOT
ROBOT
0 >> White
1 >> Black

## Slide 5: Closed Loop System
ROBOT
-ve 0 +ve
Position of the line

## Slide 6: Closed Loop System
ROBOT
-ve 0 +ve
Position of the line

## Slide 7: Closed Loop System
ROBOT
-ve 0 +ve
Position of the line

## Slide 8: CloseD Loop System
PID
  Proportional
  Integral
  Derivative
The greater the error, the greater the response.

## Slide 9: Implementing PID
ROBOT
-1 0 1
Position of the line
ROBOT
-1 0 1
ROBOT
-1 0 1

## Slide 10: Implementing PID: Hacking the IR Sensor

## Slide 11: Implementing PID
Obtaining the position of the line:
  Subtract value of left-sensor from the right-sensor
INPUT (LEFT SENSOR ¦ RIGHT SENSOR) | ERROR (Position of Line)
0 ¦ 0 | 0 – 0 = 0
1 ¦ 0 | 0 – 1 = -1
0 ¦ 1 | 1 – 0 = 1

## Slide 12: Implementing PID: P controller
Default state (Error = 0): Both wheels move forward at same speed
  Robot moves forwards
Error = 1: Left wheel spins faster than right wheel by KP * Error
  Robot turns right (while moving forward)
Error = -1: Right wheel spins faster than right wheel by KP * Error
  Robot turns left (while moving forward)
KP is the Proportional constant. Usually a +ve value.
Allows robot to react according to how large the error actually is.

## Slide 13: P Controller: Pseudo Code
float P {0}, I {0}, D {0};
setup(): - Set required pins (IR sensor pins, Motor pins)
loop(): - Read IR sensor pins >> Determine error - P = error - moveLeftMotor(BIAS + KP * P) - moveRightMotor(BIAS – KP * P)
BIAS –
Default motor speed so robot continuously moves forwards

## Slide 14: Implementing PID: I controller
Sum of errors over an interval
Defines how quick the system (robot) responds to a change from the 0 point.
  Larger change from 0 point >> Larger response
Response proportional by KI to Integral component
ROBOT
ROBOT
ROBOT
ROBOT
ROBOT
ROBOT
ROBOT
ROBOT
0
0
0
0.4
0.2
0.9
0.4
1.0

## Slide 15: Implementing PID: D Controller
Prevent overshooting by predicting future error based on rate of change.
  Higher rate of change of error >> Larger response.
Response proportional by KD to Derivative component

## Slide 16: I,D Controller: Pseudo Code
float P {0}, I {0}, D {0};
setup(): - Set required pins (IR sensor pins, Motor pins)
loop(): - Read IR sensor pins >> Determine error - P = error - I = I + error - D = error – prevError
- prevError = error - moveLeftMotor(BIAS + (KP * P + KI * D + KD * D)) - moveRightMotor(BIAS – (KP * P + KI * D + KD * D))
BIAS –
Default motor speed so robot continuously moves forwards