## Slide 1: Intro to RPi (Part 1)
By SUTD IEEE

## Slide 2: Agenda
Setting up your RPi
  Install Raspbian
  Configure Wi-Fi
  Set static IP
  Setup SSH
  Setup VNC
Using the RPi through the Terminal
Using the RPi like an Arduino
  GP I/O Pins with Python

## Slide 3: What’s an RPi?!
Single Board Computer
Runs Linux (Most of the time)
Small
  System on a Chip (SOC)
  All/ most important components are on a single chip (CPU, memory, storage, IO)
Access to GP I/O Pins (Input and Output)
  Like an Arduino

## Slide 4: Uses of RPi’s
Web Servers
Cloud Servers
Home Automation
Home Security
Arcade Games
Supercomputing (Clusters)
Cryptocurrency mining
Robotics
…

## Slide 5: Installing Raspbian on the RPi’s SD Card
Copy Etcher and the Raspbian image to your computer
Connect the microSD Card
Open Etcher
Select the Raspbian image
Click ‘Flash!’

## Slide 6: Setting Up Wi-Fi
Raspbian does not have a GUI that supports WPA2 Protocol
  Cannot connect to SUTD_Student directly!
  Need to configure it manually
Configure network in /etc/wpa_supplicant/wpa_supplicant.conf

## Slide 7: Setting Up Wi-Fi
Open Terminal
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf
Add this to the file: network={ ssid=“SUTD_Student” key_mgmt=WPA-EAP eap=PEAP identity=“100XXXX” password=“YOUR_PASSWORD” phase1=“peaplabel=0” phase2=“auth=MSCHAPV2” }
Reboot

## Slide 8: Set Static IP Address
What’s an IP(v4) Address?
Why? So we can connect to the RPi at the same address every time.
Open Terminal: ip -4 addr show | grep global ip route | grep default | awk '{print $3}’ cat /etc/resolv.conf

## Slide 9: Set Static IP Address
sudo nano /etc/dhcpcd.conf
Add this to the file: interface wlan0 static ip_address=10.1.1.31/24 static routers=10.1.1.1 static domain_name_servers=10.1.1.1
Reboot

## Slide 10: What is SSH (Secure Shell)
It is a protocol that allows a computer to remotely log in to another through the Terminal, allowing you to use that computer.
  In this case the RPi

## Slide 11: Setting up SSH
GUI
  Open ‘Applications Menu’ (Top Left) >> ‘Preferences’ >> ‘Raspberry Pi Configuration’
  Select the ‘Interfaces’ tab; enable SSH
Command Line
  Run: sudo raspi-config
  Navigate to interfaces; enable SSH

## Slide 12: Setting up VNC (Virtual Network Computing)
RealVNC – Free!
GUI
  Open ‘Applications Menu’ (Top Left) >> ‘Preferences’ >> ‘Raspberry Pi Configuration’
  Select the ‘Interfaces’ tab; enable VNC
Command Line
  Run: sudo raspi-config
  Navigate to interfaces; enable VNC

## Slide 13: Using the RPi through the Terminal
www.mprat.org/Terminus/
Learn Linux commands to navigate and control the file system.

## Slide 14: Linux Commands & Tools
cd
ls
touch
rm
mkdir
rmdir
nano/ vi
mv
cp
find
cat
ifconfig
http://www.informit.com/blogs/blog.aspx?uk=The-10-Most-Important-Linux-Commands

## Slide 15: Now for the Electronics Stuff
Program the RPi’s GP I/O Pins
  General Purpose Input/ Output
  https://pinout.xyz/#
Use it like an Arduino
Can be done using Python, C, C++, NodeJS, Bash, etc.

## Slide 16: GP I/O with Python
Install RPI.GPIO
  sudo pip install rpi.gpio
In Python
  import RPi.GPIO as GPIO

## Slide 17: GP I/O with Python
GPIO.setmode(MODE) => MODE is GPIO.BOARD or GPIO.BCM
GPIO.setup(channel, GPIO.HIGH) => channel can be a list of channels
GPIO.setup(channel, GPIO.HIGH, initial=GPIO.HIGH)
GPIO.input(channel)
GPIO.output(channel) => channel can be a list of channels
GPIO.PWM(channel,frequency)
GPIO.cleanup()

## Slide 18: Activity #1: Blinking LED
Connect +ve lead of LED (Longer leg) to BCM26
  Refer to https://pinout.xyz/# !
Connect a resistor from the –ve lead of the LED to an empty space
Connect the resistor to a GND pin
  Refer to https://pinout.xyz/# !

## Slide 19: Activity #1: Blinking LED
import RPi.GPIO as GPIO
from time import sleep
import sys
GPIO.setmode(GPIO.BCM)
GPIO.setup(26,GPIO.OUT)
GPIO.output(26,GPIO.HIGH)
sleep(1) // Sleep for 1s

## Slide 20: Activity #1: Blinking LED
Try:
while True:
# Do Something
finally:
GPIO.cleanup()
sys.exit()

## Slide 21: Activity #2: Fading LED
Connect +ve lead of LED (Longer leg) to BCM26
  Refer to https://pinout.xyz/# !
Connect a resistor from the –ve lead of the LED to an empty space
Connect the resistor to a GND pin
  Refer to https://pinout.xyz/# !

## Slide 22: Activity #2: Fading LED
pwm = GPIO.PWM(26,1000)
pwm.start(0)
pwm.ChangeDutyCycle(x)
for i in range(100):

## Slide 23: Activity #3: Push Button
Connect one end of the button to BCM26
Connect the other end on the same side to GND

## Slide 24: Activity #3: Push Button
GPIO.input(26)

## Slide 25: Activity #4
Use a push button to toggle an LED on and off!
TRY!

## Slide 26: The ENd