## Slide 1: Intro to RPi (Part 2)
By SUTD IEEE

## Slide 2: Agenda
Using the RPi through the Terminal
Using the RPi like an Arduino
  GP I/O Pins with Python
RPi Serial Communication
  Talk to an Arduino using an RPi

## Slide 3: What’s an RPi?!
Single Board Computer
Runs Linux (Most of the time)
Small
Access to GP I/O Pins (Input and Output)
  Like an Arduino

## Slide 4: Linux Commands & Tools
cd
ls
touch
rm
mkdir
rmdir
nano
mv
cp
find
cat
Ifconfig

## Slide 5: Linux Commands & Tools
http://web.mit.edu/mprat/Public/web/Terminus/Web/main.html

## Slide 6: Now for the Electronics Stuff
Program the RPi’s GP I/O Pins
  General Purpose Input/ Output
  https://pinout.xyz/#
Use it like an Arduino
Can be done using Python, C, C++, Bash, etc.

## Slide 7: GP I/O with Python
Install RPI.GPIO (In Terminal)
  sudo pip3 install rpi.gpio
In Python File
  import RPi.GPIO as GPIO

## Slide 8: GP I/O with Python
GPIO.setmode(MODE) => MODE is GPIO.BOARD or GPIO.BCM
GPIO.setup(channel, GPIO.HIGH) => channel can be a list of channels
GPIO.setup(channel, GPIO.HIGH, initial=GPIO.HIGH)
GPIO.input(channel)
GPIO.output(channel) => channel can be a list of channels
GPIO.PWM(channel,frequency)
GPIO.cleanup()

## Slide 9: Activity #1: Blinking LED
Connect +ve lead of LED (Longer leg) to BCM26
  Refer to https://pinout.xyz/# !
Connect a resistor from the –ve lead of the LED to an empty space
Connect the resistor to a GND pin
  Refer to https://pinout.xyz/# !

## Slide 10: Activity #1: Blinking LED
import RPi.GPIO as GPIO
from time import sleep
import sys
GPIO.setmode(GPIO.BCM)
GPIO.setup(26,GPIO.OUT)
GPIO.output(26,GPIO.HIGH)
sleep(1) // Sleep for 1s

## Slide 11: Activity #1: Blinking LED
Try:
while True:
# Do Something
finally:
GPIO.cleanup()
sys.exit()

## Slide 12: Activity #2: Fading LED
Connect +ve lead of LED (Longer leg) to BCM26
  Refer to https://pinout.xyz/# !
Connect a resistor from the –ve lead of the LED to an empty space
Connect the resistor to a GND pin
  Refer to https://pinout.xyz/# !

## Slide 13: Activity #2: Fading LED
pwm = GPIO.PWM(26,1000)
pwm.start(0)
pwm.ChangeDutyCycle(x) // 0 ≤ x ≤ 100
for i in range(100):
pwm.stop()

## Slide 14: Activity #3: Push Button
Connect one end of the button to BCM26
Connect the other end on the same side to GND

## Slide 15: Activity #3: Push Button
GPIO.setup(26,GPIO.IN,pull_up_down=GPIO.PUD_UP)
GPIO.input(26)

## Slide 16: Activity #3: Push Button - Debounce
Oscillation in mechanical switch in button => Multiple button presses
Logic:
  Wait for x ms after button pressed and until button is released
  Only then register it as 1 button press

## Slide 17: Activity #4: TRY It Yourself
Use a push button to toggle an LED on and off!
TRY!

## Slide 18: Serial Communication
Send data bit by bit, instead of all at once
Many protocols:
  UART / USART
  SPI
  I2C
  …

## Slide 19: Serial Communication (UART)
Universal Asynchronous Receiver-Transmitter
Star-Bit
Data Bits
Parity Bit (Optional)
Stop Bit/s

## Slide 20: Python Serial in RPI (With Arduino)
Why?
  Offload processing and simple tasks to Arduino
  Add more input/ output pins
  Connect to other serial peripherals
How?
  Connect a USB cable from the Pi to the Arduino

## Slide 21: On Arduino
String inString = “”; void serialEvent() { char c = ‘ ’; c = Serial.read(); if (c == ‘\n’) { // Do something inString = “”; } else { inString += c; } }

## Slide 22: SPI and I2C
RPi has:
  3 SPI Bus’s (Only one accessible via the headers)
  2 I2C Bus’s accessible through the headers
  I think

## Slide 23: The ENd