## Slide 1: Intro to RPi (Part 3)
By SUTD IEEE

## Slide 2: Agenda
RPi Serial Communication (Contd.)
Using Firebase with RPi (the right way)
Running a Web Server on the RPi

## Slide 3: Rpi GPIO
  https://pinout.xyz/#

## Slide 4: Activity: Push Button
Connect one end of the button to BCM26
Connect the other end on the same side to GND

## Slide 5: Activity: Push Button
GPIO.setup(26, GPIO.IN, pull_up_down=GPIO.PUD_UP)
GPIO.input(26)

## Slide 6: Activity: Push Button - Debounce
Oscillation in mechanical switch in button => Multiple button presses
Logic:
  Wait for x ms after button pressed and until button is released
  Only then register it as 1 button press

## Slide 7: Serial Communication
Send data bit by bit, instead of all at once
Many protocols:
  UART / USART
  SPI
  I2C
  …

## Slide 8: Serial Communication (UART)
Universal Asynchronous Receiver-Transmitter
Star-Bit
Data Bits
Parity Bit (Optional)
Stop Bit/s

## Slide 9: Python Serial in RPI (With Arduino)
Why?
  Offload processing and simple tasks to Arduino
  Add more input/ output pins
  Connect to other serial peripherals
How?
  Connect a USB cable from the Pi to the Arduino

## Slide 10: Python Serial in RPI (With Arduino)
Install pyserial
  sudo pip3 install pyserial
Create a Python file
  import serial
  ser = serial.Serial(‘/dev/tty*’, 9600)
  ser.write(‘Something’) >> ‘Something’ must be in bytes
Check serial port name:
  ls /dev/tty*

## Slide 11: On Arduino
String inString = “”; void serialEvent() { char c = ‘ ’; c = Serial.read(); if (c != ‘\n’) { inString += c; } else { // Do Something ! inString = “”; } }

## Slide 12: On Arduino
Seven Segment Display
  Common Anode
  Connect one of the ‘Com’ to +5V
  Connect other pins to Arduino Digital Pins
    Through RESISTORS!
+5V
12
11
9
10
8
5
7
6

## Slide 13: SPI and I2C
RPi has:
  3 SPI Bus’s (Only one accessible via the headers)
  2 I2C Bus’s accessible through the headers
  I think

## Slide 14: Firebase (The Right way)
‘Database Secrets’ is deprecated
‘python-firebase’ module not updated in 4 years
The right way?
  Firebase Admin SDK (Python)

## Slide 15: FIREBASE (THE RIGHT WAY)
Open your Firebase Console
Navigate to Project Settings >> Service Accounts
Generate new Private Key >> Save that file in your project folder

## Slide 16: FIREBASE (THE RIGHT WAY)
In the Firebase Console:
Open Database Tab
Navigate to ‘Rules’
Change it to this: { "rules": { ".read": "auth.uid === ‘some_UID’”, ".write": "auth.uid === ‘some_UID’” } }
Publish

## Slide 17: Firebase (The Right way)
How to install?
  sudo pip3 install firebase-admin
Create a Python file
  import firebase_admin
  from firebase_admin import credentials
  from firebase_admin import db

## Slide 18: FIREBASE (THE RIGHT WAY)
cred = credentials.Certificate(‘PATH_TO_KEY')
firebase_admin.initialize_app(cred, {
'databaseURL': 'https://your_database.firebaseio.com/',
'databaseAuthVariableOverride': {
'uid': ‘your_uid'
}
})

## Slide 19: FIREBASE (THE RIGHT WAY)
To use the database:
  mydatabase = db.reference()
  Get:
    mydatabase.get()
    mydatabase.child(‘some_child’).get()
  Set:
    mydatabase.child(‘some_child’).set( { “key”: “value” } )
  Update
  Push

## Slide 20: FIREBASE (THE RIGHT WAY)
Refer to the template to learn how to continuously get a certain database entry

## Slide 21: Firebase (The Right Way)
Your task:
  Write another file that asks for an input and updates a particular database entry using .set() -> On your computer
  Run a script on the RPi to continuously read that same database entry and based on that asks the Arduino to display said input on the 7-Segment Display

## Slide 22: Flask Server
Flask is a Python framework that allows you to manage your web servers
  It is not a web server! (Though it comes with one by default)
Install:
  virtualenv:
    sudo pip3 install virtualenv
    mkdir myproject
    cd myproject
    virtualenv myvenv
    . myvenv/bin/activate
  flask:
    pip3 install Flask

## Slide 23: Flask Server
Refer to ‘flaskapp’ in Templates for example

## Slide 24: The ENd