## Slide 1: http://tinyurl.com/SUTDIEEEWorkshops (Dropbox) => Intro to RPi Series => Part 1 Windows Users: Download & Install MobaXTerm (For SSH) (Or your own choice of SSH Client) Mac Users: Don’t need anything

## Slide 2: Intro to RPi (Part 1)
By SUTD IEEE
http://tinyurl.com/SUTDIEEEWorkshops

## Slide 3: Agenda
Setting up your RPi
  Install Raspbian
  Configure Wi-Fi
  Set static IP
  Setup SSH
  Setup VNC
Using the RPi through the Terminal
Using the RPi like an Arduino
  GP I/O Pins with Python

## Slide 4: What’s an RPi?!
Single Board Computer
Runs Linux (Most of the time)
Small
  System on a Chip (SOC)
  All/ most important components are on a single chip (CPU, memory, storage, IO)
Access to GP I/O Pins (Input and Output)
  Like an Arduino

## Slide 5: Uses of RPi’s
Web Servers
Cloud Servers
Home Automation
Home Security
Arcade Games
Supercomputing (Clusters)
Cryptocurrency mining
Robotics
…

## Slide 6: Installing Raspbian on the RPi’s SD Card
Copy Etcher and the Raspbian image to your computer
Connect the microSD Card
Open Etcher
Select the Raspbian image
Click ‘Flash!’

## Slide 7: Setting Up Wi-Fi
Raspbian does not have a GUI that supports WPA2 Protocol
  Cannot connect to SUTD_Student directly!
  Need to configure it manually
Configure network in /etc/wpa_supplicant/wpa_supplicant.conf

## Slide 8: Setting Up Wi-Fi
Open Terminal
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf
Add this to the file: network={ ssid=“SUTD_Student” key_mgmt=WPA-EAP eap=PEAP identity=“100XXXX” password=“YOUR_PASSWORD” phase1=“peaplabel=0” phase2=“auth=MSCHAPV2” }
Reboot

## Slide 9: Set Static IP Address
What’s an IP(v4) Address?
Why? So we can connect to the RPi at the same address every time.
Open Terminal: ip -4 addr show | grep global ip route | grep default | awk '{print $3}’ cat /etc/resolv.conf

## Slide 10: Set Static IP Address
sudo nano /etc/dhcpcd.conf
Add this to the file: interface wlan0 static ip_address=10.1.1.31/24 static routers=10.1.1.1 static domain_name_servers=10.1.1.1
Reboot

## Slide 11: What is SSH (Secure Shell)
It is a protocol that allows a computer to remotely log in to another through the Terminal, allowing you to use that computer.
  In this case the RPi

## Slide 12: Setting up SSH
GUI
  Open ‘Applications Menu’ (Top Left) >> ‘Preferences’ >> ‘Raspberry Pi Configuration’
  Select the ‘Interfaces’ tab; enable SSH
Command Line
  Run: sudo raspi-config
  Navigate to interfaces; enable SSH

## Slide 13: Setting up VNC (Virtual Network Computing)
RealVNC – Free!
GUI
  Open ‘Applications Menu’ (Top Left) >> ‘Preferences’ >> ‘Raspberry Pi Configuration’
  Select the ‘Interfaces’ tab; enable VNC
Command Line
  Run: sudo raspi-config
  Navigate to interfaces; enable VNC

## Slide 14: Using the RPi through the Terminal
www.mprat.org/Terminus/
Learn Linux commands to navigate and control the file system.

## Slide 15: Linux Commands & Tools
cd
ls
touch
rm
mkdir
rmdir
nano/ vi
mv
cp
find
cat
ifconfig
http://www.informit.com/blogs/blog.aspx?uk=The-10-Most-Important-Linux-Commands

## Slide 16: Now for the Electronics Stuff
Program the RPi’s GP I/O Pins
  General Purpose Input/ Output
  https://pinout.xyz/#
Use it like an Arduino
Can be done using Python, C, C++, NodeJS, Bash, etc.

## Slide 17: GP I/O with Python
Install RPI.GPIO (In Terminal)
  sudo pip3 install rpi.gpio
In Python File
  import RPi.GPIO as GPIO
Documentation
  https://sourceforge.net/p/raspberry-gpio-python/wiki/Examples/

## Slide 18: GP I/O with Python
GPIO.setmode(MODE) => MODE is GPIO.BOARD or GPIO.BCM
GPIO.setup(channel, GPIO.HIGH) => channel can be a list of channels
GPIO.setup(channel, GPIO.HIGH, initial=GPIO.HIGH)
GPIO.input(channel)
GPIO.output(channel) => channel can be a list of channels
GPIO.PWM(channel,frequency)
GPIO.cleanup()

## Slide 19: Activity #1: Blinking LED
Connect +ve lead of LED (Longer leg) to BCM26
  Refer to https://pinout.xyz/# !
Connect a resistor from the –ve lead of the LED to an empty space
Connect the resistor to a GND pin
  Refer to https://pinout.xyz/# !

## Slide 20: Activity #1: Blinking LED
import RPi.GPIO as GPIO
from time import sleep
import sys
GPIO.setmode(GPIO.BCM)
GPIO.setup(26,GPIO.OUT)
GPIO.output(26,GPIO.HIGH)
sleep(1) // Sleep for 1s

## Slide 21: Activity #1: Blinking LED
Try:
while True:
# Do Something
finally:
GPIO.cleanup()
sys.exit()

## Slide 22: Activity #2: Fading LED
Connect +ve lead of LED (Longer leg) to BCM26
  Refer to https://pinout.xyz/# !
Connect a resistor from the –ve lead of the LED to an empty space
Connect the resistor to a GND pin
  Refer to https://pinout.xyz/# !

## Slide 23: Activity #2: Fading LED
pwm = GPIO.PWM(26,1000)
pwm.start(0)
pwm.ChangeDutyCycle(x) // 0 ≤ x ≤ 100
for i in range(100):
pwm.stop()

## Slide 24: Activity #3: Push Button
Connect one end of the button to BCM26
Connect the other end on the same side to GND

## Slide 25: Activity #3: Push Button
GPIO.setup(26,GPIO.IN,pull_up_down=GPIO.PUD_UP)
GPIO.add_event_detect(channel, GPIO.FALLING)
if GPIO.event_detected(channel): #Do Something

## Slide 26: Activity #3: Push Button - Debounce
Oscillation in mechanical switch in button => Multiple button presses
Logic:
  Wait for x ms after button pressed and until button is released
  Only then register it as 1 button press

## Slide 27: Activity #3.1: TRY It Yourself
Use a push button to toggle an LED on and off!
  Press button => LED turns on & remains on
  Press button again => LED turns off & remains off
TRY!
Hint: You are going to need to keep track of the state of the LED (is it current on/ off)
Syntax
  if (SOME STATEMENT): # Do Something

## Slide 28: Activity #4: 7-Segment Driver
Choose 7 I/O Pins on the Raspberry Pi
Connect 7 resistors to the 7-Segment display
Connect wires
Code is the same as controlling an LED, just 7 of them!

## Slide 29: Activity #4: 7-Segment Driver
Creating a function in Python:
  def my_function(param1, param2): ## Your function goes here
Getting user input:
  my_input = input(“Write something: ”)

## Slide 30: Serial Communication
Send data bit by bit, instead of all at once
Many protocols:
  UART / USART
  SPI
  I2C
  …

## Slide 31: Serial Communication (UART)
Universal Asynchronous Receiver-Transmitter
Star-Bit
Data Bits
Parity Bit (Optional)
Stop Bit/s

## Slide 32: Python Serial in RPI (With Arduino)
Why?
  Offload processing and simple tasks to Arduino
  Add more input/ output pins
  Connect to other serial peripherals
How?
  Connect a USB cable from the Pi to the Arduino

## Slide 33: On Arduino
String inString = “”; void serialEvent() { char c = ‘ ’; c = Serial.read(); if (c == ‘\n’) { // Do something inString = “”; } else { inString += c; } }

## Slide 34: SPI and I2C
RPi has:
  3 SPI Bus’s (Only one accessible via the headers)
  2 I2C Bus’s accessible through the headers
  I think

## Slide 35: The ENd