## Slide 1: Intro to RPi (Part 2)
By SUTD IEEE

## Slide 2: Agenda
Using Firebase with RPi (the right way)
Running a Web Server on the RPi

## Slide 3: Rpi GPIO
  https://pinout.xyz/#

## Slide 4: ACTIVITY SETUP
Connect +ve lead of LED (Longer leg) to BCM26
  Refer to https://pinout.xyz/# !
Connect a resistor from the –ve lead of the LED to an empty space
Connect the resistor to a GND pin
  Refer to https://pinout.xyz/# !

## Slide 5: Firebase (The Right way)
‘Database Secrets’ is deprecated
‘python-firebase’ module not updated in 4 years
The right way?
  Firebase Admin SDK (Python)

## Slide 6: FIREBASE (THE RIGHT WAY)
Open your Firebase Console
Navigate to Project Settings >> Service Accounts
Generate new Private Key >> Save that file in your project folder

## Slide 7: FIREBASE (THE RIGHT WAY)
In the Firebase Console:
Open Database Tab
Navigate to ‘Rules’
Change it to this: { "rules": { ".read": "auth.uid === ‘some_UID’”, ".write": "auth.uid === ‘some_UID’” } }
Publish

## Slide 8: Firebase (The Right way)
How to install?
  sudo pip3 install firebase-admin
Create a Python file
  import firebase_admin
  from firebase_admin import credentials
  from firebase_admin import db

## Slide 9: FIREBASE (THE RIGHT WAY)
cred = credentials.Certificate(‘PATH_TO_KEY')
firebase_admin.initialize_app(cred, {
'databaseURL': 'https://your_database.firebaseio.com/',
'databaseAuthVariableOverride': {
'uid': ‘your_uid'
}
})

## Slide 10: FIREBASE (THE RIGHT WAY)
To use the database:
  mydatabase = db.reference()
  Get:
    mydatabase.get()
    mydatabase.child(‘some_child’).get()
  Set:
    mydatabase.child(‘some_child’).set( { “key”: “value” } )
  Update
  Push

## Slide 11: FIREBASE (THE RIGHT WAY)
Refer to the template to learn how to continuously get a certain database entry

## Slide 12: Firebase (The Right Way)
Your task:
  Write another file that asks for an input (on/off) and updates a particular database entry using .set() -> On your computer
  Run a script on the RPi to continuously read that same database entry and based on that turn an LED on/off.

## Slide 13: Flask Server
Flask is a Python framework that allows you to manage your web servers
  It is not a web server! (Though it comes with a test server for … well, testing)
Install:
  virtualenv:
    sudo pip3 install virtualenv
    mkdir myproject
    cd myproject
    virtualenv myvenv
    . myvenv/bin/activate
    To deactivate: type deactivate
  flask:
    pip3 install Flask
    To run: type flask run –-host=0.0.0.0 -–port=8080

## Slide 14: Flask Server
Refer to ‘flaskapp.zip’ in for example

## Slide 15: The ENd