## Slide 1: Communication protocols with Arduino
SUTD IEEE Student Chapter

## Slide 2: Agenda
Theory
  What are they?
  Why do I need them?
  How do I use them?
Practical
  Hooking up some devices to the Arduino with Serial Comm.

## Slide 3: What Are Serial Communication Protocols
Method of sending (and receiving) data and that is serialized, to other devices or peripherals.
Protocols specify how exactly the data is sent, how exactly the device is supposed to be connected, how fast it should send data, etc.
Three different serial communication protocols on Arduino:
  TTL Serial
  SPI
  I2C

## Slide 4: Why Do I need these communication Protocols
Arduino supports both Digital and Analogue OUTPUTS and INPUTS
  Connect sensors such as LDRs, Ultrasonic sensors, etc.
  Control components such as motors, LEDs, etc.
What about more complex devices such as accelerometers, LCDs, controlling LED displays?

## Slide 5: Why Do I need these communication Protocols
Communication Protocols allow transfer of data between devices
Eg. Use an LCD by specifying the coordinates of a pixel to be turned on or off.

## Slide 6: Brief Summary of Communication Protocols on Arduino
TTL Serial | SPI | I2C
Asynchronous | Synchronous | Synchronous
Between 2 devices | 1 Master to many Slaves | Many Masters to many Slaves (Max 121 for Arduino)
TX/ RX Pins | MOSI, MISO, SCK, SS | SDA, SCL
Fast | Very fast | Not that fast
Common applications: GPS, Bluetooth Modules Microcontrollers | Common applications: Sensors, Touchscreens, Control devices (eg. Digital Pots), Memory, LCD | Common applications: Small LCD/ OLED, Sensors, EEPROMs, Display connectors

## Slide 7: But Before That …
What exactly is serial data?
  Sequence of binary digits (1’s and 0’s) sent one after another to form (usually) 8-bit binary numbers (sequence of 8 - 1’s and 0’s)
  These numbers can then be converted to decimal or interpreted as ASCII or Unicode characters.

## Slide 8: Binary Data
Which bit is sent first – right most bit or left most bit?
  Little vs Big Endian

## Slide 9: How to use communication protocols
TTL Serial
SPI
I2C

## Slide 10: TTL Serial
Can be asynchronous or synchronous – Arduino is asynchronous
  Asynchronous
    Communication synchronized with start/stop bits (messages)
  Synchronous
    Communication synchronized with external clock
Stands for Transistor-Transistor Logic
Notes: Why is synchronization important?

## Slide 11: TTL Serial
Uses a UART as a hardware intermediary
  Can also be implemented via software (bit-banging) i.e. Arduino SoftwareSerial Library
Star-Bit
Data Bits
Parity Bit (Optional)
Stop Bit(s)

## Slide 12: TTL Serial - Transmitting

## Slide 13: TTL Serial - Transmitting

## Slide 14: TTL Serial - Receiving

## Slide 15: TTL Serial - Receiving
inStr.toInt()

## Slide 16: SPI
Serial Peripheral Interface
  Synchronous Interface
Uses a Master-Slave concept
Allows 1 Master to many Slaves
Multiple-Masters not possible

## Slide 17: SPI
Data structure is very simple
No start bit, stop bit, or parity bit
Very fast!
Data is sent on rising or falling edge of clock cycle.

## Slide 18: SPI with Arduino
Arduino Uno (ATMega328P) has one SPI Bus
Uses library <SPI.h>
  #include at the start
Using the library:
  SPI.begin() // Does not take any parameters
  SPISettings(SPEED, DATAORDER, DATAMODE)
For understanding: http://dlnware.com/dll/Clock-Phase-and-Polarity

## Slide 19: SPI with Arduino
Using the library:
  SPI.beginTransaction(SPISettings)
  SPI.transfer(DATA)
  SPI.endTransaction()
  SPI.end()
  SPI.usingInterrupt(PIN)

## Slide 20: SPI with Arduino
Can be used to control a shift register – which allows a sequence of bits to be ‘shifted’ and set a series of (usually) 8 outputs on or off
  Thus, they ‘expand’ the Arduino’s output pins
ST_CP goes to ground
DS goes to MOSI
SH_CP goes to SCK

## Slide 21: SPI - TRY IT OUT
Call SPI.begin() in setup()
In loop():
  Create a loop to count from 0 to 255 and write that data to the shift register via SPI.transfer()
  Execute SPI.beginTransaction(SPISettings(1000,MSBFIRST,SPI_MODE0)) before the transfer and execute SPI.endTransaction() after

## Slide 22: SPI - Final Code

## Slide 23: SPI - Challenge
Try to make a Decade counter with this setup
  Only one LED on at a time

## Slide 24: I2C
Inter-Integrated Circuit
Only 2 Wires – SDA (Serial Data) and SCL (Serial Clock)
How? Using an address (7-8 bits) per device connected
  Connect 120 devices at once! (8 reserved addresses)
Is able to identify which device is sending or receiving data

## Slide 25: I2C on Arduino
SDA – A4
SCL – A5
If connecting with device that runs on 3.3 V, pull SDA and SCL pins to high (5V) via a resistor

## Slide 26: I2C on Arduino
<Wire.h>
begin()
requestFrom()
beginTransmission()
endTransmission()

## Slide 27: I2C on Arduino
write()
available()
read()
SetClock()
onReceive()
onRequest()

## Slide 28: I2C on Arduino
ADXL345
  https://learn.sparkfun.com/tutorials/adxl345-hookup-guide?_ga=2.1431734.625444

## Slide 29: I2C on Arduino
[Go through demo]

## Slide 30: I2C on Arduino
Adafruit has written a great library to use the ADXL345, but what’s going on in the background?
I2C is used to read from / write to particular memory address in the ADXL345 which contain info about accelerometer data, temperature, etc. and other configuration options.

## Slide 31: ADXL345 I2C Datasheet
https://www.sparkfun.com/datasheets/Sensors/Accelerometer/ADXL345.pdf Pages 10 and 14

## Slide 32: Summary of Communication Protocols Learnt Today
TTL Serial | SPI | I2C
Asynchronous | Synchronous | Synchronous
Between 2 devices | 1 Master to many Slaves | Many Masters to many Slaves (Max 121 for Arduino)
TX/ RX Pins | MOSI, MISO, SCK, SS | SDA, SCL
Fast | Very fast | Not that fast
Common applications: GPS, Bluetooth Modules Microcontrollers | Common applications: Sensors, Touchscreens, Control devices (eg. Digital Pots), Memory, LCD | Common applications: Small LCD/ OLED, Sensors, EEPROMs, Display connectors (HDMI, VGA, etc.)

## Slide 33: Serial Communication
There are so many others for different purposes!
  Short range vs long range
  Fast vs slow
  Easy vs complex
  …
Just visit the Wikipedia page and find out more!

## Slide 34: Thank You for Coming