## Slide 1: Basic Intro To Arduino’s https://tinyurl.com/2018DHWSRes
Presented by SUTD IEEE Student Branch

## Slide 2: Arduino
Open source platform for Microcontrollers
Easy to program/ reprogram the ATmega328P Microcontroller in C++
Loads of built in functions for easy manipulation of ports!
ATmega328P

## Slide 3: Arduino – ATMEGA328P
Refer to http://www.circuitstoday.com/basics-of-microcontrollers for more info!

## Slide 4: Arduino – what can it do?
Read ‘Inputs’ and set ‘Outputs’
2 types on ‘Inputs’ and 2 types of ‘Outputs’

## Slide 5: Arduino – what can it do?
Inputs
  Digital
    ON – 5V / HIGH
    OFF – 0V / LOW
  Analogue
    Continuous value between 0V-5V
Outputs
  Digital
    ON – 5V / HIGH
    OFF – 0V / LOW
  Pulse with Modulated (PWM)
    Square Wave with variable duty cycle

## Slide 6: Arduino – What can it do?

## Slide 7: Arduino and Electronics
Pictorial Diagrams!
  Uses images of how the components look in real life
  Shows how the connections physically look
Schematic Diagrams!
  Uses standard symbols to represent electronic components
  Shows exact connections and offers more detail

## Slide 8: Arduino and Electronics: Quick Physics Recap
+
LOAD
-
GND

## Slide 9: Arduino and Electronics: Breadboard
Columns Connected
Rows Connected
Not Connected

## Slide 10: Arduino and Electronics: Jumper Wires
Male-Male Wire
Male-Female Wire
Female-Female Wire

## Slide 11: Arduino and Electronics: Resistors
Resistors are one of the most used components
So remember this table!
(Or just search for a resistor calculator, like a sane person!)

## Slide 12: Arduino and Electronics: LED’s
LED’s are polarized – only work one way
+ve Leg to HIGH, -ve Leg to GND
How do you identify which is which?
  Short leg is -ve OR
  -ve end has a flat side

## Slide 13: Arduino and Electronics: Potentiometers
Variable resistor
Allows you to divide voltage potential.
Arduino can measure voltage at center pin.
5v
Gnd
Divided Voltage

## Slide 14: Arduino and Electronics: Buttons
Digital Input
Either 1 or 0
End 1
End 4
End 2
End 3

## Slide 15: Great Lets Play!
… but first, we need to understand how to program the Arduino.

## Slide 16: Uploading to the Arduino
Open up the blink example sketch!
There is a built in LED on the Arduino board so we will not have to make any circuit (yet)

## Slide 17: Uploading to the Arduino
Select the port that access Arduino!
If there are multiple ports:
Unplug Arduino, check port
Plug in Arduino, pick the new port

## Slide 18: Uploading to the Arduino
Check the board selected
We are using the Arduino Uno

## Slide 19: Uploading to the Arduino
Verify
Upload

## Slide 20: Coding Basics
Many different programming languages, some low-level, some high-level.

## Slide 21: Coding Basics
Many general concepts apply across (most) languages (at least high-level ones)
Many languages: C, C++, C#, Python, Java, MatLab, Go, JavaScript, etc…
What is a program?
  It generally defines a set of instructions to be carried out by the computer or system that is intended to produce a given output, perhaps given an input. How this can be done is discussed on the next slide.

## Slide 22: Coding Basics: General Concepts
Variables
  Containers for data
  Types:
    Int, Float, Bool(ean), Double, Char, String, and many more
Functions
  Just like mathematical functions. Give an input (sometimes), and get an output (sometimes)
Loops
  Do-While, While, For
  Control statements: break, continue, etc…
(type of variable) (name of variable) = (assignment);

## Slide 23: Coding Basics: General Concepts
Conditionals
  if (CONDITION) … then … else …
Operations
  Bitwise
    |, &, >>, <<, ^, ~
  Logical
    <, >, <=, >=, !=, ==, &&, ||
  Arithmetic
    +, -, /, *, ^, %

## Slide 24: Coding Basics: C++
{ … } – Curly brackets define a block of code that is executed
  Variables defined within the brackets are only accessible in those brackets and any brackets inside (Local and global scope)
( … ) – Round brackets enclose parameters
; – Every line of code terminates with a semi-colon – denotes end of ‘sentence’!
// – Single line comment
/* … */ – Multi line comment

## Slide 25: Programming for the Arduino
Arduino uses C++
Two main functions:
  setup()
    Runs once
  loop()
    Runs again and again until something goes wrong or the Arduino turns off
void setup () {
….
….
} It runs the code once upon start-up
void loop () {
….
….
}
It runs the code continuously after setup.

## Slide 26: Programming for the Arduino – Arduino Specific Functions
void setup()
void loop()
delay()
pinMode()
Serial.begin() and Serial.println()
digitalRead() and digitalWrite()
analogRead() and analogWrite()

## Slide 27: Programming for the Arduino – Arduino Specific Functions
delay(x)
  Stops execution of any code for x milliseconds.
  delay(500); // Delay for 500ms
Serial
  Serial.begin()
  Serial.print()
  Serial.println()

## Slide 28: Programming for the Arduino – Arduino Specific Functions
Serial.begin(x)
  Begins connection via the serial protocol to the attached device (e.g. your computer)
  Sets communication speed at x bits/s
  Common speed: 9600 bits/s
  Set speeds: 9600, 14400, 19200, 38400, 57600, 115200, 128000, 256000, etc.

## Slide 29: Programming for the Arduino – Arduino Specific Functions
Serial.print()
  Uses the serial protocol to send characters to your computer
  Serial.print(“Hello world);
  Serial.print(35);
Serial.println()
  Exactly the same as Serial.print() but adds a ‘\n’ (newline) character at the end of your ‘sentence’
  Serial.println(“Hello world);

## Slide 30: Programming for the Arduino – Arduino Specific Functions
pinMode(x, MODE)
  Tells the Arduino that pin x is going to be an OUTPUT / INPUT
  pinMode(3, OUTPUT);
  pinMode(A0, INPUT);
digitalRead(x)
  Reads value on input pin x – returns 0 or 1
  int inputValue = digitalRead(3);
digitalWrite(x, MODE)
  Writes value on output pin – HIGH or LOW
  digitalWrite(3, HIGH)

## Slide 31: Programming for the Arduino – Arduino Specific Functions
analogRead(x)
  Reads analog value on input pin x – returns 0 – 1023
  int inputValue = analogRead(A0);
analogWrite(x, y)
  Writes value on output pin x – with a value of y (0 – 255)
  digitalWrite(3, HIGH)

## Slide 32: Alright, Time for some Arduino!

## Slide 33: ACTIVITY #1: DIGITAL OUTPUT – Blinking The LED
Connect a wire from pin 6 to a resistor.
Connect an LED to the resistor (long leg first)
Connect a wire from the LED (short leg) to a GND pin.

## Slide 34: ACTIVITY #1: DIGITAL OUTPUT – Blinking The LED

## Slide 35: ACTIVITY #2: ANALOG Output – Fading The LED
Same circuit as before.
Use analogWrite() instead of digitalWrite()
Employ for loops.
Continuous output.
Only pins with a ‘~’ sign next to them support PWM (via hardware)
  For the UNO: 3, 5, 6, 9, 10 and 11

## Slide 36: ACTIVITY #2: ANALOG Output – Fading The LED

## Slide 37: Activity #3: Analog Input – LIGHT SENSOR
Resistance of the LDR changes with light
  Due to ratio of R1 and LDR, voltage across R1 will change
Arduino will measure change in voltage and determine whether it is currently dark or bright

## Slide 38: Activity #3: Analog Input – LIGHT SENSOR
Logic:
  If too dark: turn on light
  If too bright: turn off light
    What we need is a threshold and check if sensor value is less than or greater than threshold.
  Does sensor value increase with light brightness? Or does it decrease?

## Slide 39: Activity #3: Analog Input – LIGHT SENSOR

## Slide 40: Extra Activity: Digital Input – Buttons
Toggle the state of the LED when button is pressed
Press button once
  LED turns on
Press button again
  LED turns off
Use digitalRead()

## Slide 41: Summary
What is an Arduino?
Programming in C++ (for Arduino)
Basic electronics (analog vs digital)
Inputs and Outputs
Programming the Arduino

## Slide 42: Thank You for coming https://tinyurl.com/2018DHWS
Courtesy of SUTD IEEE Student Branch